## Slide 1
제조사
MODEL
NAME
ADAMSON
CS10P
LINE ARRAY SPEAKER
2-WAY, FULL RANGE INTELLIGENT LOUDSPEAKER
Frequency Range (+/- 3dB) : 60 Hz - 18 kHz
Nominal Directivity (-6 dB) H x V : 70° x 40° or 100° x 50°
Maximum Peak SPL : 139 dB
Components LF : 2x ND10-LM 10” Kevlar Neodymium Driver
Components HF : Adamson NH3 3” Diaphragm / 1.4” Exit Compression Driver
Rigging : Integrated Rigging System
: Built-in Polemount Socket
Connections
Power : powerCON TRUE1
Network : 2 x etherCON
Analog : 2 x XLR
Dimension (WxHxD) : 326.6/192 x 744 x 444.5mm
Weight : 30kg
Amplification : 2 channel Class-D, 2400 W total output
Input Voltage : 100 - 240 V
Current Draw at 230 V : 0.45 A rms idle, 1.6 A rms long-term, 10 A max peak
Processing : Onboard / Proprietary