## Slide 1
제조사
MODEL
NAME
DPA
4018
SUSPENSION MICROPHONE
Supercardioid Microphone
Directional pattern : Supercardioid
Principle of operation : Pressure gradient
Cartridge type : Pre-polarized condenser
Frequency response : 20 Hz - 20 kHz
Effective frequency range, ±2 dB, at 30 cm (11.8 in) : 40 Hz - 18 kHz
Sensitivity, nominal, ±2 dB at 1 kHz : 12 mV/Pa; -38.4 dB re. 1 V/Pa
Distortion, THD < 1% : 134 dB SPL RMS, 137 dB SPL peak
Dynamic range : Typ. 121 dB
Max. SPL, THD 10% : 156 dB SPL peak
Switchable attenuator, filters etc. : 0 dB / -20 dB
Rated output impedance : 200 Ω
Minimum load impedance : 2 kΩ
Common mode rejection ratio (CMRR) : > 60 dB
Connector : XLR-3M. Pin 1: shield, Pin 2: signal + phase, Pin 3: - phase
Color : Matte black
Weight : 158 g (5.6 oz)
Microphone diameter : 19 mm (0.75 in)
Capsule diameter : 19 mm (0.75 in)
Microphone length : 170 mm (6.7 in)