## Slide 1
제조사
MODEL
NAME
DPA
4166
HEADSET MICROPHONE
Flex Omnidirectional Headset and Earset Microphone
Directional pattern : Omnidirectional
Principle of operation : Pressure
Cartridge type : Pre-polarized condenser
Frequency response : 20 Hz - 20 kHz
Effective frequency range ±2 dB : 40 Hz - 20 kHz with 3 dB soft boost at 8 - 15 kHz
Sensitivity, nominal, ±3 dB at 1 kHz : 6 mV/Pa; -44 dB re. 1 V/Pa
Distortion, THD < 1% - CORE : 134 dB SPL RMS, 137 dB SPL peak
Dynamic range - CORE : Typ. 111 dB
Max. SPL, THD 10% : 144 dB SPL peak
Rated output impedance : 30 - 40 Ω
Connector : MicroDot, TA4F Mini-XLR, 3-pin LEMO, Mini-Jack
Color : Black, beige or brown
Microphone diameter : 5.4 mm (0.21 in)
Microphone Boom length
Normal : 120 mm (4.7 in)
Medium : 100 mm (3.9 in)
Cable length : 1.3 m (4.3 ft)
Cable color : Black, beige or brown
Cable diameter : 1.6 mm (0.06 in)