## Slide 1
제조사
MODEL
NAME
DPA
6061
PIN MICROPHONE
Subminiature Microphone
Directional pattern : Omnidirectional
Principle of operation : Pressure
Cartridge type : Pre-polarized condenser
Frequency response : 20 Hz - 20 kHz
Effective frequency range ±2 dB : 40 Hz - 20 kHz with 4 dB soft boost at 8 - 20 kHz
Sensitivity, nominal, ±3 dB at 1 kHz : 6 mV/Pa; -44 dB re. 1 V/Pa
Equivalent noise level, A-weighted : Typ. 26 dB(A) re. 20 μPa (max. 28 dB(A))
Distortion, THD < 1% : 125 dB SPL RMS, 128 dB SPL peak
Dynamic range : Typ. 102 dB
Max. SPL, THD 10% : 144 dB SPL peak
Rated output impedance : 30 - 40 Ω
Connector : MicroDot, TA4F Mini-XLR, 3-pin LEMO, Mini-Jack
Color : Black, beige, brown or white
Weight : 8 g (0.29 oz) incl. Cable and MicroDot connector
Microphone head size (h x w x d) : 3.4 / 14.4 mm (0.13 / 0.57 in)
Capsule diameter : 3 mm (0.12 in)
Cable length : 1.8 m (5.9 ft)