## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
C28:4
POWER AMP
4ch POWER AMPLIFIER
Number of channels : 4
Peak total output all channels driven : 2800 W
Peak output voltage per channel : 141 V
Max. output current per channel : 12 Arms
Max. Output Power (Per ch. (all ch.’s driven) / Bridged per ch.
- 16 ohms : 600 W / 1400 W
- 8 ohms : 700 W / 1200 W
- 4 ohms : 700 W / 600 W
- 2 ohms : 300 W / n.r
- Hi-Z : 700 W (70 Vrms / 100 V peak) / 1400 W (140 Vrms / 200 V peak)
Performance with Gain: 35 dB and VPL: 100 V
- THD 20 Hz - 20 kHz for 1 W : <0.1%
- THD at 1 kHz and 1 dB below clipping : <0.05%
- Signal To Noise Ratio : >112 dBA
- Channel separation (Crosstalk) at 1 kHz : >70 dB
- Frequency response (1 W into 8 ohms) +0/-3 dB : 6.8 Hz - 34.2 kHz
- Input impedance : 20 kOhm
- Common Mode Rejection (CMR) : >50 dB
- Output impedance @ 100 Hz : 30 mOhm
Dimensions (WxHxD) / Weight : 483 x 88 x 343 mm / 12 kg