## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
D20:4L
POWER AMP
4ch DSP POWER AMPLIFIER
Processing / Network : Lake / Dante
Number of amplifier channels : 4
Total burst power all channels : 2000 W
Max. Output Power (all ch.’s driven)
- 2 ohms : 500 W
- 2.67 ohms : 500 W
- 4 ohms : 500 W
- 8 ohms : 500 W
- 16 ohms : 425 W
- Hi-Z 25 V : 500 W
- Hi-Z 70 V : 500 W
- Hi-Z 100 V : 250 W
THD + N 20 Hz - 20 kHz for 1 W : < 0.05 %
THD + N at 1 kHz and 1 dB below clipping : < 0.04 %
Dynamic range : > 112 dB
Channel separation (Crosstalk) at 1 kHz : > 70 dB
Frequency response (1 W into 8 ohm, 20 Hz - 20 kHz) : +/- 0.05 dB
Internal sample rate / Data path : 96 kHz / 32 bit floating point
Product propagation delay AES 96 kHz / analog input : 1.61 / 1.68 ms
Dimensions (WxHxD) / Weight : 483 x 44 x 425 mm / 7.9 kg