## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
FP10000Q
POWER AMP
4ch POWER AMPLIFIER
Number of channels : 4
Peak total output both channels driven : 10000 W
Peak output voltage per channel : 150 V
Max. output current per channel : 50 A peak
Max. Output Power (2/4/8/16ohms)
- Per ch. (both ch.’s driven) : 2500 W / 2100 W / 1300 W / 660 W
- Bridged per ch. : n.r. / 5000 W / 4200 W / 2600 W
Performance with Gain: 35 dB and VPL: 150 V
- THD 20 Hz - 20 kHz for 1 W : <0.1%
- THD at 1 kHz and 1 dB below clipping : <0.05%
- Signal To Noise Ratio : >112 dBA
- Channel separation (Crosstalk) at 1 kHz : >70 dB
- Frequency response (1 W into 8 ohms) +0/-3 dB : 6.8 Hz - 34 kHz
- Input impedance : 20 kOhm
- Common Mode Rejection (CMR) : >54 dB, 20 Hz to 20 kHz
- Output impedance @ 100 Hz : 32 mOhm
Dimensions (WxHxD) : 483 x 88 x 396 mm
Weight : 12 kg
Finish : Black painted steel chassis with black painted steel / aluminum front