## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
LUCIA 240/2
POWER AMP
POWER AMPLIFIER
Number of powered channels : 2
Total output all channels driven : 240 W
Max output voltage per channel : 43.8 V peak
Max. output current per channel : 7.8 Arms
Max. Output Power (all ch.’s driven)
- 2 ohms : 120 W
- 4 ohms : 120 W
- 8 ohms : 120 W
- 16 ohms : 60 W
THD 20 Hz - 20 kHz at 1 W into 8 ohms: <0.3%
THD at 1 kHz and 1 dB below clipping : <0.2%
Signal To noise ratio into 8 ohms : >101 dBA
Channel separation (Crosstalk) at 1 kHz : >60 dB
Frequency response : 5 Hz - 22 kHz
Input impedance : 10 kOhm
Input common mode rejection, CMR : 40 dB
Connectors
- Input connectors (per ch.) : 3-pin detachable screw terminals, electronically balanced
- Input connectors (ch 1 & 2) : Unbalanced RCA type
- Output connectors (per ch.) : 2-pin detachable screw terminals
Dimensions (WxHxD) : 216 x 44 x 280 mm
Weight : 1.9 kg
Finish : Black aluminum front and black steel chassis