## Slide 1
제조사
MODEL
NAME
LAB.GRUPPEN
PDX3000
POWER AMP
POWER AMPLIFIER
Number of amplifier channels : 2
Number of processing channels : 2
Peak total output all channels driven : 3000 W
Peak output voltage per channel : 115 V
Peak output current per channel : 32 A
Bridge mode : No
Output circuit type : Class-D
Max Output Power All channels driven
- 2 Ω per channel : 1000 W
- 4 Ω per channel : 1500 W
- 8 Ω per channel : 800 W
THD+N 20 Hz - 20 kHz @ 1 W : < 0.1%
THD+N @ 1kHz, 1 dB below clip : < 0.1%
Signal-to-noise : >90 dB
Channel separation (Crosstalk) @ 1 kHz : >75 dB
Frequency response : 10 Hz to 20 kHz, +0.5/ -1 dB
Input impedance : 10 kΩ unbalanced, 20 kΩ balanced
Internal Sample rate : 96 kHz
Product propagation delay : 0.6 ms
Distortion,1/8 rated power : < 0.1%
Dimensions (HxWxD) : 93 x 483 x 326 mm
Weight : 6.5 kg
Finish : Black painted aluminium chassis and grey front