## Slide 1
제조사
MODEL
NAME
MIDAS
HUB4
PERSONAL MONITOR HUB
Monitor System Hub with 4 PoE Ports for Personal Mixers
Connections
AES50 sync master / thru : 2 x RJ45
AES50 remote outputs : 4 x RJ45
Remote power : PoE (IEEE802.3at)
USB : Type B
StageConnect : 1 x XLR, male
Analogue outputs : 4 x XLR, balanced / 12 x 1/4" TRS, balanced
AES50
Audio channels : 48
Sample rate : 44.1 / 48 kHz
Sample word length : 24 bit
Clock synchronization : AES50 Sync Master
Latency : min. 70 µs per node (AES50)
Cable : shielded CAT 5e
Cable length : up to 80 m (recommended)
Power Supply
Switch mode power supply : Autorange, 100-240 V~50/60 Hz
Power consumption : 180 W
Mains connection : Standard IEC receptacle
Dimensions / Weight
Dimensions (H x W x D) : 50 x 482 x 291 mm (1.97 x 18.98 x 11.46")
Weight : 8.72 lbs / 3.96 kg